## Slide 1: CSC 143
Two' s complement

## Slide 2: 10's complement
How to represent negative numbers?
  Use a sign → but −0 is the same as +0
  10's complement
Example pick a number of digits (sign + magnitude): e.g. 3 positive numbers: +18 → 018 negative numbers: −18 → 982
Why?

## Slide 3: −18 in 10's complement
Start with the positive number (3 digits) 018
Write the 9's complement (0→9, 1→8, etc.) 981
To get the 10's complement, add 1 982
Same as doing 1000 – 18
With 3 digits, 900 to 999 is -100 to -1 000 to 099 is 0 to 99

## Slide 4: What about 0?
Using 3 digits
+0 is 000
-0? 000 (+0) 999 (9's complement) 999 + 1 = 000 + carry = 1(10's complement) Always ignore the carry, so -0 is 000
Same as +0

## Slide 5: Rules
Positive numbers start with 0
Negative numbers start with 9
Apply the usual rules of arithmetic e.g. with 3 digits:
  25 – 30 = 025 + 970 = 995 995 is the usual -5 (995 = 1000 – 5)
  -10 -15 = 990 + 985 = 2975 (ignore the carry!). 975 is the usual -25
Overflow if the carry going into the sign digit (0 or 9) is not equal to the carry coming out of it. Remedy → use more digits.
X

## Slide 6: 2's complement
Positive numbers start with 0 e.g with 4 digits 7 is 4 + 2 + 1 = 1112 = 01112
Negative numbers? Start with the positive value: +7 -> 01112 1's complement: 1000 2's complement (add 1): 1001 (= -8 + 1)
Positive numbers start with 0, negative numbers start with 1

## Slide 7: Examples
Rules:1 + 1 = 10 (0, carry =1)
      0 + 1 = 1, 1 + 0 = 1, 0 + 0 = 0
      Ignore any carry out of the sign bit (overflow?)
37 + 19 (with 8 digits) = 56
-37 + 19 (with 8 digits) = -18
37 = | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
19 = | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
56 = | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0
-37 = | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
19 = | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
-18= | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0

## Slide 8: Overflow
100 + 50 (with 8 digits) = 150 (too big!)
The carry into the sign bit is +1 ≠ carry out of the sign bit is 0
Fix: use 9 digits
100 = | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
50 = | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
overflow! | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
100 = | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
50 = | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
150 = | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0

## Slide 9: What about multiplication?
Works as usual if the number of digits is enough to accommodate the answer
With 3 digits: -3 = 101, -4 = 100
However, -4 x -3 = 12 = 011002 doesn't fit into 3 digits
Fix: sign extend -3 and -4 to as many bits as necessary
How many? Safe approach: here, double the number of digits. In our example, switch to 6 digits
-4 = 111100, -3 = 111101
Do the multiplication and keep only the last 6 digits for all operations = 001100

## Slide 10: Rules (1)
For any number, can always remove all 0's or all 1's on the left except the last 0 and 1: 000110 is 0110 (= +6) 111011 is 1011 (= -5)
To convert to decimal form
  If positive: 01101 = 23 + 22 + 20 = 13
  If negative: 10111 -24 + 22 + 21 + 20 = -9 or convert to positive: 1's complement = 01000 2's complement = 01000 + 1 = 01001 and 01001 = 23 + 20 = 9 so 10111 = -9

## Slide 11: Rules (2)
Addition: a + b
  Pad a and b on the left to max( number of digits of a, number of digits of b) + 1 → never any overflow, always ignore any outgoing carry on the leftmost digits.
  -5 = 1011 (4 digits) -3 = 101 (3 digits) pad to max(4,3) + 1 = 5 -5 + -3 = 11011 + 11101 11 11 10 11 01 + 01 01 01 00 01 --------------- 01 01 00 00 00 (the outgoing carry = 1 on the leftmost digits is ignored) 11000 = 1000 = -8

## Slide 12: Rules (3)
Multiplication: a × b
  Pad a and b on the left to m = number of digits of a + number digits of b: never any overflow, always ignore any outgoing carry on the leftmost digits, for all steps work with just m digits
  -5 = 1011 (4 digits) -3 = 101 (3 digits) work with 4 + 3 = 7 digits for all operations -5 × -3 = 0001111 = 01111 = 15
11 11 11 11 10 11 01 × 01 01 01 01 01 00 01 -------------------- 11 11 11 11 10 11 01 + 11 11 10 11 11 1. 0. -------------------- 11 11 10 10 11 11 01 + 11 10 11 11 1. 1. 0. -------------------- 1 10 11 11 11 11 11 01 + 10 11 11 1. 1. 1. 0. -------------------- 1 11 11 10 11 11 11 01 + 11 11 1. 1. 1. 1. 0. -------------------- 1 1 10 10 11 11 11 01 + 11 1. 1. 1. 1. 1. 0. -------------------- 1 0 10 10 11 11 11 01